## Slide 1
Logical Network Diagram (Layer 2 / VLANs)
Site Addressing: 10.0.X.0/24 per VLAN (SiteNumber = 0)
Gateway scheme per VLAN: GW1 .1 | GW2 .2 | GW3 .3 | VIP (HSRP/VRRP) .20
Ranges: Fixed .21–.99 | DHCP .100–.199 | Reserved .200–.254

## Slide 2
Internet
External
ISP / Provider
VLAN 1
10.0.1.0/24
Edge Firewall/Router
NAT / VPN
Security policy
Default route
CORE-SW1
L3 Core
HSRP/VRRP Primary
CORE-SW2
L3 Core
HSRP/VRRP Secondary
VIP per VLAN: 10.0.<VLAN>.20
Access Switches
User/AP/Camera/Phone ports
Trunks to core
OOB Mgmt Switch
VLAN 12
Server iDRAC/iLO
VLANs / Subnets (10.0.<VLAN>.0/24)
VLAN 2 — Hosts
10.0.2.0/24
VLAN 3 — Staff Radio
10.0.3.0/24
VLAN 4 — Power Infrastructure
10.0.4.0/24
VLAN 5 — Technical Clients
10.0.5.0/24
VLAN 6 — Infrastructure Servers
10.0.6.0/24
VLAN 7 — Telephony
10.0.7.0/24
VLAN 8 — HVAC Infrastructure
10.0.8.0/24
VLAN 9 — Storage
10.0.9.0/24
VLAN 10 — NetMan (Mgmt)
10.0.10.0/24
VLAN 11 — Security Cameras
10.0.11.0/24
VLAN 12 — Server OOBM
10.0.12.0/24
VLAN 15 — Routers
10.0.15.0/24
VLAN 16 — Links / Transit
10.0.16.0/24